## Slide 1: Computer Security Principles
Securing Wireless Network
COMP6824001
Session 10

## Slide 2: These slides have been adapted from: Panek, Crystal. (2019). Security Fundamental, John Wiley & Sons, Inc. Indianapolis. ISBN: 978-1-119-65066-9 Lesson 4
Acknowledgement

## Slide 3: - Service Set Identifier (SSID) - Understanding Keys - MAC Filters - The Advantages and Disadvantages of Specific Security Types - Wireless Security - Mobile Device Security - IEEE 802.11i Wireless LAN Security
Sub Topics

## Slide 4: Service Set Identifier (SSID)
The most basic component of the wireless network is the SSID (Service Set IDentifier).
The SSID is defined in the IEEE 802.11 standard as a name for the WLAN. It does not provide any inherent security capabilities, although specifying the SSID name of the WLAN you want to connect to will ensure that you connect to the correct WLAN.
The Service Set Identifier (SSID) is a case-sensitive text string with a max length of 32 characters that can be made up of either letters, numbers, or both.
Figure: Example of SSID WiFi
Notes: https://www.javatpoint.com/service-set-identifier-in-computer-network

## Slide 5: Understanding Keys
The best available security mechanism for securing a WLAN is to use authentication and encryption. WLANs provide three key-based security mechanisms to provide that security.
WEP (Wired Equivalent Privacy)
WPA (Wi-Fi Protected Access)/WPA2 (Wi-Fi Protected Access Version 2)
Notes: Crystal Panek, page 140-143

## Slide 6: WEP (Wired Equivalent Privacy)
Wired Equivalent Privacy (WEP) is a security standard for wireless networks or WiFi.
The very first security capability available to WLAN users was WEP (Wired Equivalent Privacy)
WEP was included as part of the original IEEE 802.11 standard and was intended to provide privacy.
The flaw in WEP makes it relatively easy for an attacker to crack the encryption and access the wireless network, so it is generally only used if no other solution is available (WEP is better than nothing) or the WLAN is being used with older devices, or devices like PDAs or handheld games that require the use of WEP.
Notes: Crystal Panek, page 140-143

## Slide 7: WPA (Wi-Fi Protected Access)/WPA2 (Wi-Fi Protected Access Version 2)
WPA (Wi-Fi Protected Access) was designed as the interim successor to WEP.
The WPA protocol implements most of the IEEE 802.11i standard.
WPA2 (Wi-Fi Protected Access version 2) is the standards-based version of WPA, except WPA2 implements all the IEEE 802.11i standards.
WPA/WPA2 functions in two modes:
  Shared-Key WPA
  IEEE 802.1x
Notes: WPA (Wi-Fi Protected Access) was designed as the interim successor to WEP. The WPA
protocol implements most of the IEEE 802.11i standard. This was included in the updated
WLAN standard. IEEE 802.11i addressed a number of the issues inherent to the original
IEEE 802.11 standard. WPA included a new security protocol, Temporal Key Integrity
Protocol (TKIP), which, while related to WEP to ensure backwards compatibility, adds new
features to help address the issues associated with WEP. Unfortunately, because TKIP uses
the same underlying mechanism as WEP, it is also vulnerable to similar attacks. The number
of attacks is significantly less than with WEP, but they still exist.

## Slide 8: Understanding MAC Filters
A MAC address is the unique hardware address of a network adapter.
MAC address can be used to control what systems are able to connect to a WLAN through the use of MAC filters.
By turning MAC filtering on, network access can be limited to only permitted systems by entering the MAC address information into the MAC filters.
The table of permitted MAC addresses is maintained by the wireless access points.
Mac address is shown in the format of 00:00:00:00:00:00 or 00-00-00-00-00-00.

## Slide 9: The Advantages and Disadvantages of Specific Security Types
WEP is a solution that, while better than no security at all, is not particularly secure. The vulnerabilities within the WEP protocols encryption scheme make it very easy to crack. WEP will keep neighbors from connecting to a home WLAN, but will not slow a determined attacker very much.
WPA/WPA2 is the best security method for both home and corporate WLAN security. In pre-shared key mode, WPA/WPA2 can secure the WLAN with a passcode that is shared by the clients and the wireless access points
MAC address filtering is a good solution for a home or small office environment but has significant challenges as the number of permitted devices grows. Manually maintaining a table of MAC addresses becomes a significant challenge when there are more than 10–20 devices, especially in dynamic environments where systems are being purchased and decommissioned regularly
Notes: +
>Smaller Routing Tables
>Highly Scalable
>More Efficient Use of Network Bandwidth
>Faster Convergence

## Slide 10: Wireless Security
Some of the key factors contributing to the highersecurity risk of wireless networks compared to wired networks include the following:
  Channel
    Wireless networks are alsomore vulnerable to active attacks that exploit vulnerabilities in communications protocols.
  Mobility
    Wireless devices are, in principal and usually in practice, far more portable andmobile than wired devices. This mobility results in a number of risks, described subsequently.
  Resources
    Some wireless devices, such as smartphones and tablets, have sophisticatedoperating systems but limited memory and processing resources with which to counter threats,including denial of service and malware.
  Accesbility
    Some wireless devices, such as sensors and robots, may be left unattended inremote and/or hostile locations

## Slide 11: MOBILE DEVICE SECURITY
Mobile devices need additional, specialized protection measures beyond those implemented forother client devices, such as desktop and laptop devices that are used only within theorganization’s facilities and on the organization’s networks.
NIST SP 800-124 (Guidelines forManaging the Security of Mobile Devices in the Enterprise, June 2013) lists seven major securityconcerns for mobile devices.
There are security threats, includes:
  Lack of Physical Control
  Use of Untrusted Mobile Devices
  Use of Untrusted Networks
  Use of Untrusted Applications
  Interactions with other Systems
  Use of Untrusted Content
  Use of Location Services
Notes: https://www.kaspersky.com/resource-center/threats/what-is-a-honeypot

## Slide 12: IEEE 802.11i Wireless LAN Security
There are two characteristics of a wired LAN that are not inherent in a wireless LAN.
  In order to transmit over a wired LAN, a station must be physically connected to the LAN. On the other hand, with a wirelessLAN, any station within radio range of the other devices on the LAN can transmit. In a sense, there is a form of authenticationwith a wired LAN, in that it requires some positive and presumably observable action to connect a station to a wired LAN.
  Similarly, in order to receive a transmission from a station that is part of a wired LAN, the receiving station also must be attachedto the wired LAN. On the other hand, with a wireless LAN, any station within radio range can receive. Thus, a wired LANprovides a degree of privacy, limiting reception of data to stations connected to the LAN.
Notes: https://www.fortinet.com/resources/cyberglossary/what-is-dmz

## Slide 13: IEEE 802.11i Wireless LAN Security
The 802.11i RSN security specification defines the following services:
  Authentication: A protocol is used to define an exchange between a user and an AS (authentication server) that provides mutualauthentication and generates temporary keys to be used between the client and the AP over the wireless link.
  Access control: This function enforces the use of the authentication function, routes the messages properly, and facilitates keyexchange. It can work with a variety of authentication protocols.

## Slide 14: References
Panek, Crystal. (2019). Security Fundamental, John Wiley & Sons, Inc. Indianapolis. ISBN: 978-1-119-65066-9
Stallings, William and Lawrie Brown. 2018. Computer Security: Principles and Practice, 4th Edition. Global Edition, Pearson Education Limited
Notes: Resources:
https://www.cloudflare.com/learning/ddos/glossary/open-systems-interconnection-model-osi/
https://www.cloudflare.com/learning/ddos/glossary/open-systems-interconnection-model-osi/
https://learningnetwork.cisco.com/s/contentdocument/0693i000001r6HTAAY
https://www.cloudflare.com/learning/network-layer/what-is-ipsec/
https://www.hypr.com/security-encyclopedia/transport-mode#:~:text=Transport%20Mode%20is%20a%20method,Transport%20Mode%20or%20Tunnel%20Mode.
https://www.ibm.com/docs/en/zos/2.2.0?topic=encapsulation-transport-mode-tunnel-mode
https://docs.oracle.com/cd/E36784_01/html/E36838/ipsecov-13.html
https://www.hypr.com/security-encyclopedia/tunnel-mode#:~:text=Tunnel%20Mode%20is%20a%20method,address%20information%20is%20also%20encrypted.